## Slide 1: AutoCAD 2D_I
Module 4: Isometric Drawing

## Slide 2: Module Objectives
Explain the difference between Isometric and oblique drawing.
Correctly produce an isometric drawing for cubes, circles, and cylinders
Correctly produce oblique drawings for cubes, circles and cylinders.
Draw isometric and oblique drawings for a combination of cubes, circles, and cylinders.

## Slide 3: Introduction

## Slide 4: Introduction
The pictorial drawing is a three dimensional drawing that shows an object’s three principal planes, much as they would be captured by a camera.

## Slide 5: Types of Pictorial drawing
There are three types of pictorial drawings Isometric, Oblique, and perspective. In this module only Isometric and Oblique will be dealt with.

## Slide 6: Types of Pictorial drawing
Perspective
Oblique
Isometric
Next

## Slide 7: Isometric Pictorial Drawing
Isometric drawing represents an object in three dimensions. It helps to visualize the features of an object on at least three sides. The three axes forms an angle of 120 degrees between one another
Back

## Slide 8: Oblique Pictorial Drawing
Oblique projection is a form of parallel projection in which the projectors are parallel to each other but are not perpendicular to the projection plane. Two types of oblique drawing are shown below
Back
CAVALIER
CABINET

## Slide 9: Perspective Pictorial Drawing
Watch the following Video about perspective drawing, and try to redraw the same drawing as a self study homework.
Perspective pictorial drawing
Back

## Slide 10
In this Module, we’re Going to study about the Isometric Pictorial drawing and the Oblique pictorial drawing
Oblique Drawing
Isometric Drawing

## Slide 11: Isometric drawing
Drawing a cube
Drawing circles or cylinders
Next

## Slide 12: Isometric drawing of a cube
1. Draw two basic 30 degree (to the horizontal line) guidelines, one to the left and one to the right, plus a vertical guideline in the centre of the drawing as shown in the figure below. This will guide the isometric drawing of the cube. The required tools are shown below
Next

## Slide 13: Isometric drawing of a cube
2. Draw guidelines to help start constructing the left and right sides of the cube. Remember to use a 30 degree set square for the 'angled' lines. See the figure below
Next

## Slide 14: Isometric drawing of a cube
3. The top of the cube can be drawn quite easily by using the set square to draw one edge of the top and then ‘flipping’ it over to draw the other. See the figure below
Next

## Slide 15: Isometric drawing of a cube
4. The Final isometric drawing of the cube is shown in the figure below
Next

## Slide 16: Isometric drawing of a cube
For More Clarification, you can Visit the following Link which will help you draw an isometric cube
http://www.technologystudent.com/designpro/isomet1.htm
Back

## Slide 17: Isometric drawing of circles and cylinders
1. Construct an isometric square 60 mm by 60mm mm using 30, and 60 degree set square as shown in the figure below. The isometric square will be used to draw the isometric circle.
Next

## Slide 18: Isometric drawing of circles and cylinders
2. Construct a perpendicular bisector from each side of the isometric square, then draw two perpendicular bisectors (center lines) from each midpoint as shown on the Fig.4.9.
Next

## Slide 19: Isometric drawing of circles and cylinders
3. Locate the two centers. By campus draw the two arcs as shown on the Figure.
Next

## Slide 20: Isometric drawing of circles and cylinders
4. Draw the arcs with these centers and tangent to isometric square. The final front side isometric circle (ellipse) is shown on the Figure
Next

## Slide 21: Isometric drawing of circles and cylinders
5. The isometric circle (Ellipse) in Front, Right and Top views is shown in the figure.
Next

## Slide 22: Isometric drawing of circles and cylinders
6. Drawing an isometric cylinder will be simply by drawing two isometric circles opposite to each other and then connecting them together. i.e: top and bottom or front and back …etc.
Back

## Slide 23: Oblique drawing
Oblique projection is a method of drawing objects in 3 dimensions. It is quite a simple technique compared to isometric drawing. In the Oblique drawing instead of the two 30 degrees guide lines, there are one horizontal line and one 45 degrees guidelines accordingly; the 45 degrees set square is an important drawing tool while drawing oblique drawings.

## Slide 24: Oblique drawing
Drawing a cube
Drawing circles or cylinders
Next

## Slide 25: Oblique drawing of a cube
The required tools are shown in the figure below
Next

## Slide 26: Oblique drawing of a cube
1. Draw the front or side view of the object Remember to use a T-square and 45 degree set square. See the figure
Next

## Slide 27: Oblique drawing of a cube
2. Draw 45 degree lines from each corner of the square. The distance of any lines drawn back at 45 degrees should be halved (cabinet). For example, a cube may have sides of 100mm but they must be drawn 50mm in length. The cube will look more realistic and in proportion. See the figure
Next

## Slide 28: Oblique drawing of a cube
3. Draw the vertical and horizontal lines to complete the drawing of the cube. See the figure.
Back

## Slide 29: Drawing cylinders in oblique projection
Drawing cylinders in the oblique projection is quite simple if the stages outlined below are followed. In comparison with other ways of drawing cylinders (for example, perspective and isometric) using oblique projection is relatively easy.
Next

## Slide 30: Drawing cylinders in oblique projection
1. Draw a vertical and horizontal centre lines to indicate the centre of a circle, then use a compass to draw the circle. See the figure
Next

## Slide 31: Drawing cylinders in oblique projection
2. Draw a 45 degree line to match the length on the cylinder. At the end of this line draw vertical and horizontal centre lines. See the figure
Next

## Slide 32: Drawing cylinders in oblique projection
3. The general rule for oblique is to half all distances projected backwards. If the cylinder is 100mm in length the distance back must be drawn to 50mm. See the figure
Next

## Slide 33: Drawing cylinders in oblique projection
4. The final shape is shown in the figure
Back

## Slide 34: Activities

## Slide 35: Activities
Class Work Activities
Homework Activities
Next

## Slide 36
Next

## Slide 37
Back

## Slide 38
Next

## Slide 39
Back

## Slide 40: The End